## Slide 1: SAFEX
Video Analytics System (VAS) for Marine Systems, Platform Systems Sustainment Centre, HTX
May Intern Brief

## Slide 2: Base Layout
3 places of interest
Camera Locations:
  Hangar
  Outside Hangar/Bay Area
  Oil Storage Area
Cameras at different locations will run different VAs
System Deployment – Office Area
Arrange for site visit this week*

## Slide 3
POC Stage | Feature | Details | Alert Type | POC location | Notes
SafeX 1.0 Target start :Early Feb 2024 Target completion: July 2024 | Detection of proper donning of PPE within PPE restricted zones. | Detection if workers are wearing proper PPE in PPE restricted zone (i.e. hanger etc) | Immediate | Hanger | 
 | Detection of Forklift operation | When forklift is in operation, send an alert to everyone. | Immediate | Hanger, walkways | 
 | Unauthorised access during operation of crane | Check if human and vehicle (forklift) enter hanger during operation | Immediate | Hanger | 
 | Counting of oil drums and detection of oil drum movements and oil drum leaks | Alert on changes of oil drums count and the person moving the drum | Immediate | Oil storage area | This will be a security feature to ensure that all oil drums are accounted for
 | Illegal Parking | Alert if vehicle is stationary near the hanger for too long | Immediate | Outside Hanger | 
Phase 1

## Slide 4
SafeX 2.0 Target start :July 2024 Target completion: Jan 2025 | Feature | Description | Alert Type | POC Location | 
 | Stacking of objects in a hazardous manner | Alert if object is stacked beyond safe height threshold | Immediate | Hanger | 
 | Obstruction of walkway or any other unsafe conditions such as oil/ water puddles etc | To detect and notify of any unsafe conditions that may arise within the workshop/ walkways and hangers | Immediate | hanger, walkways | 
 | Safe operation of crane | Check if Load hung for too long Load is unbalanced Shaky movement (both vertical and horizontal) | Immediate | Hanger | 
 | Detection of any human horseplaying/ object left at hanger/ service bay area (Housekeeping) | Human detection such as: Running, skipping, cycling, using of machines etc. Leaving materials, tools, other items within | Immediate | Hanger, Work shed | 
Phase 2

## Slide 5
SafeX 3.0 (additional features) | Feature | Description | Alert Type | POC Location | 
 | Detection of diving operations | Detection of diving operations and training activities within service bay area. | Immediate | Service Bay | 
 | Facial Recognition | To detect the person entering/ moving around a restricted area/ unauthorized access. | Immediate | Hanger | 
Phase 3

## Slide 6: Infrastructural Info
Platform: GPU-enabled Laptop
Streaming Method: RTSP Stream
Network: LAN Network using Router
Range: ~100m from furthest camera to system

## Slide 7: Useful Tools
Docker Image
Python with OpenCV
PyTorch and CUDAToolKit
YOLOv8 or other object detection models
SORT based tracking algorithms
ResNet or other object classification models

## Slide 8: Milestones 1
Milestone 1: 5th June
  Implement PPE Detection with extensive testing
  Implement Unauthorized Access with extensive testing
  Implement Simple User Interface to integrate above
  Dockerize above solution
  Testing with CCTV Camera on LAN
Milestone 2: 28th June
  Combine the remaining phase 1 functions
  Extensive testing on all functions